AAR Origin Quality Review

Bi-Level Post Loading Inspector Test

- What is the maximum distance primary grate lock chock side paddle should be from vehicle tire.

- ½” to ¾”.

- 1” to 1 ¾”.

- Tire contact to ¾”.

- None of the above.

- What is the proper number of Holden Grip lock chocks to be used to secure a vehicle?

A. 2.

B. 3.

C. 8.

D. 6.

- Is primary Holden chock usable with the red or green locking tab missing.

- Yes.

- No.

- If a bi-level is equipped with supplemental (AVR or Holden block chocks) are they required to be used at your facility?

- Yes.

- No.

- What is the proper distance between a grate lock chock face plate and the vehicle tire?

- ½” to ¾”.

- 1” to 1 ¾”.

- Tire contact to ¾”.

- None of the above.

Bi-Level Post Loading Inspector Test Continued

6. When securing a vehicle with the Holland VRS chock with blue strap, does it matter if vehicle tire, strap and chock are positioned on the same grate section.

A. Yes.

B. No.

7. When securing a vehicle with the Holland VRS chock with blue strap at one position, the strap cleat should be at:

A. 9 o’clock.

B. 1 o’clock.

C. 11 o’clock.

D. none of the above.

8. What does the green tell-tale indicator on Holden grip lock chock indicate.

A. Chock Locked.

B. Chock unlocked and ready to remove.

C. Front teeth locked.

D. none of the above.

9. What is a minimum distance between vehicles on multi-level when the vehicles are secured?

A. 2”.

B. 3” Only if loading pattern will not allow for additional spacing.

C. 5”.

D. 4”.

10. What is the minimum distance required to the closest point of contact from a vehicle to a multi-level end door.

A. 7”.

B. 3”.

C. 5”. Only if loading pattern will not allow for additional spacing.

D. 4”.

Bi-Level Post Loading Inspector Test Continued

11. Which drawing below shows the proper loading pattern for placing vehicles in a multi-level?

A

B

12. What is the proper setting for an automatic transmission once a vehicle is loaded on a multi-level?

A. Park.

B. Neutral.

C. Reverse.

D. Does not matter.

13. Is it a requirement to ensure the parking brake is engaged once a vehicle is loaded on a multi-level?

A. Yes.

B. No.

14. Can different chock types be used to secure individual vehicles on multi-levels?

Yes.

No.

15. When vehicles are loaded on grate bi-level multi-levels, the vehicles should be centered on the multi-level deck. What is the farthest a vehicle can be positioned off center and not be an exception?

A. 3”.

B. 5”.

C. 2”.

D. none of the above.

Bi-Level Post Loading Inspector Test Continued

16. Tools used inside loaded multi-levels must be covered to protect vehicles from damage. What is the allowable amount of exposed metal on a tool used for prying?

A. 1”.

B. 2”.

C. 3”.

D. No exposed metal is allowed.

17. What is the proper height setting for grate chocks used to secure vehicles?

A. Refer to the manufacturers vehicle loading publication.

B. 2” of clearance from any part of the vehicle to the chock once installed.

C. Both A and B.

18. When installing extra chocks (inboard between the front and rear tires). The chock side paddles must be positioned away from the vehicle tire side walls?

A. Yes.

B. No.

19. Referring to the figure below. During the installation inspection, if a Holden grate chock is found to have deformed or straightened grate latch teeth is the chock useable.

A. Yes.

B. No.

Bi-Level Post Loading Inspector Test Continued

20. All extra chocks not used to secure vehicles must be properly stored when loading and securing vehicles.

A. Yes.

B. No.

21. Chocks must be properly placed on multi-level decks to ensure the same chock type are used to secure individual vehicles prior to the vehicles being loaded.

A. Yes.

B. No.

Origin Quality Review

Tri-Level Post Loading Inspector Test

- What is the maximum distance a tri-level chock can be from a vehicle tire.

- Contact to 1”.

- Contact to 2”.

- ½” to 1”.

- 3”.

- Contact required.

- When using Co-Polymer chocks, are you required to tighten both chocks?

- Yes.

- No.

- At what position should the 3 cleats be positioned on a vehicle tire?

- 10/12/2.

- 9/11/1.

- 12/2/4.

- None of the Above.

- What is the proper tension for a Co-Polymer chock?

- Compress the vehicle tire plus 2 clicks.

- Snug up both chocks then two additional clicks on both chocks.

- Tighten up both chocks as much as you can.

- Tighten each chock until it stops lifting off the deck.

AAR Origin Quality Review

Tri-Level Post Loading Inspector Test - Continued

- How should the strap be positioned on the vehicle tire?

- On the tire tread near the front as you are looking at it.

- On the tread at the center of the tire cleats down.

- On the tread at the center of the tire cleats up.

- None of the above.

- Is a cracked Co-Polymer chock still usable?

- Yes.

- No.

- Is a Co-Polymer chock missing a “C” clip or thumb locking handle usable?

- Yes.

- No.

8. What does the green tell-tale indicator on Holden grip lock chock indicate?

A. Chock Locked.

B. Chock unlocked and ready to remove.

C. Front teeth locked.

D. none of the above.

9. What is the minimum distance between vehicles on multi-level when the vehicles are secured?

A. 2”.

B. 3” Only if loading pattern will not allow for additional spacing.

C. 5”.

D. 4”.

AAR Origin Quality Review

Tri-Level Post Loading Inspector Test - Continued

10. What is the minimum distance required to the closest point of contact from a vehicle to a multi-level end door?

A. 7”.

B. 3”.

C. 5”. Only if loading pattern will not allow for additional spacing.

D. 4”.

11. Which drawing below shows the proper loading pattern for placing vehicles in a multi-level?

A

B

12. What is the proper setting for an automatic transmission once a vehicle is loaded on a multi-level?

A. Park.

B. Neutral.

C. Reverse.

D. Does not matter.

13. Is it a requirement to ensure the parking brake is engaged once a vehicle is loaded on a multi-level?

A. Yes.

B. No.

14. Can different chock types be used to secure individual vehicles on multi-levels?

Yes.

No.

AAR Origin Quality Review

Tri-Level Post Loading Inspector Test - Continued

15. When vehicles are loaded on tri-level multi-levels, the vehicles should be positioned on the multi-level decks no closer than ½” from the 3rd rail chock locking track and to allow the strap/harness to be placed in the center of the tire tread?

A. Yes.

B. No.

D. none of the above.

16. Tools used inside loaded multi-levels must be covered to protect vehicles from damage. What is the allowable amount of exposed metal on a tool used for prying?

A. 1”.

B. 2”.

C. 3”.

D. No exposed metal is allowed.

17. All extra chocks not used to secure vehicles must be properly stored when loading and securing vehicles.

A. Yes.

B. No.

18. Chocks must be properly placed on multi-level decks to ensure the same chock type are used to secure individual vehicles prior to the vehicles being loaded.

A. Yes.

B. No.